## Slide 1: Porting IPN2220AP on Embedded System
SW Engineer:Yeh, Chih Hao,
Embedded System
Inprocomm, Inc, Taiwan

## Slide 2: Inprocomm, System Vendor’s Porting Efforts
Inprocomm
  provides IPN2220.o, which contains object code compiled from OS-independent source code.
  Consultation on porting, performance tuning.
System Vendor
  Register ISR, network interface with respective OS
  Calling API provided by IPN2220.o
  Provides KAL logic
  Provides 802.1X solution

## Slide 3: Porting Work Flow
Inprocomm introduces on KAL-logic and porting(2 – 4 hrs).
System vendor prepares KAL-logic and registers with OS. Inprocomm reviews wlan_kal.h in the mean time.(1 week)
System vendor does WPA Porting(1 – 2 week)
Inprocomm and System vendor work on tuning performance and testing.(variable)

## Slide 4: KAL: Kernel Abstract Layer
A layer between Operating System and IPN2220.o driver object code.
By modifying this kernel abstract layer, it is easy to port IPN2220 AP driver into a new platform.

## Slide 5
IPN2220 Driver
KAL-Logic
Embedded OS
Register IF
Call i2220ap_priv_create
Call i2220ap_pci_probe
Register ISR
Call i2220hw_interrupt
HW Interrupt
Call do_isr_tasklet
kal_netif_rx
transmit packet
I2220ap_hard_xmit
kal_free_skb
kal_alloc_skb
IPN2220
Driver
Life
Cycle
kal_free_skb

## Slide 6: KAL Logic
Cacheable memory allocation
  kal_malloc_sz(), kal_free(),
Non-cacheable and DMA-accessible memory allocation
  kal_pci_alloc_sz, kal_pci_free_sz
Net packet allocation and free
  kal_alloc_skb,kal_free_skb
Mapping virtual address to bus address
  kal_pci_map_single, kal_pci_unmap_single
PCI memory register read/write
  kal_pci_readl, kal_pci_writel

## Slide 7: Data path
Packet Transmitting
  OS calls KAL’s TX callback.
  KAL prepares network packet compliant with Inprocomm’s network packet model
  KAL calls i2220ap_hard_xmit()
Packet Reception
  OS calls KAL’s ISR, then KAL schedules to call do_isr_tasklet()
  do_isr_tasklet() calls kal_netif_rx().
  KAL prepares net packet compliant with OS and indicate it upward.

## Slide 8: Inprocomm’s Net Packet Model
Packet content must be virtually and physically continuous. Its content should be non-cacheable.
Upper layer send net packet in Ethernet format.
IPN2220 indicates received wireless packet in Ethernet format.
Dest. 6 byte | Src. 6 byte | Prtcl. | Payload

## Slide 9: Inprocomm’s Net Packet Model
Net packet should be able
  1. to return its current content starting address via kal_skb_data()
  2. to return its current content length via kal_skb_len()
  3. to support kal_skb_pull to trim packet beginning; kal_skb_push to make room in the beginning; kal_skb_put to set packet’s content length.

## Slide 10: AP operating mode
Switch mode(default)
  IPN2220 driver handles station-to-station traffic.
Switch mode with no relay between stations
  IPN2220 driver stops forwarding packet between stations
Data pipe
  IPN2220 driver indicates all station’s data frame upward and does not forward packets between WLAN stations.

## Slide 11: WPA
IPN2220 Drivers provides
  Hardware key management and (de)encryption
  TKIP MIC calculation and failure notification.
  802.1X port on/off mechanism
  WPA Capability announcement in beacon
System vendor handles
  802.1X Frame exchange(certification and 4-way handshake)
  WPA-PSK pass phrase calculation
  Station WPA capability parsing
  Counter measure

## Slide 12: I/O Control on IPN2220
All these function can be commanded through param_xx_xx and cmd_xx_xx functions listed in wlan_lib.h
Including
  Basic AP function
  WDS
  Key and WPA mechanism
  Statistics and network information

## Slide 13: Conclusion
Inprocomm accumulates knowledge on porting IPN2220 driver to different OS and network protocol stack.
Inprocomm provides a clear-cut interface.
Inprocomm can help System Vendor speed up porting IPN2220 driver.